Penn 7600

Dual Base Instructions

- Use the BASE key to select ‘Base2’ on the display. If a container will be used to hold the parts being sampled, place it on the platform at this time.

- Press the SAMPLE key. The scale zeros.

“AddXXX” appears on the display.

Repeated pressing of the SAMPLE key

successively displays the five sample sizes.

3. The sample may now be placed onto the scale all at

the same time. *The more parts that are added, the

lower the percent of error.

4. Select the BASE key to select ‘Base1’.

(BASE2 on the display disappears).

a.) If you would like to enter the known tare weight

of a full container, use the number keypad then

press the TARE key. You may now add the full

container of remaining pieces to be counted at

this time.

b.) If you are adding pieces to an empty container,

place container onto scale, the press the ZERO

key. You may now add the remaining pieces to

be counted at this time.